## Slide 1
Lab Book 2.0. Couplers
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/cifoin-lab2.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  COUPLERS_Student.ipynb
Cross-Sections to be studied:
h
(height)
w (width)
Core
Cladding
w (width)
MMI Body
Cladding
Multimode Interference (MMI) coupler
Directional coupler (DC)
Core
g
(gap)
h
(height)

## Slide 3
Directional coupler

## Slide 4: Learning outcome #1 – Directional coupler cross-section in GDSFactory
INSTRUCTOR:
Present Python and GDSFactory implementation of DC cross-section
Describe how to obtain the beating length
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, gap between waveguides 0.6 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 5: Learning outcome #2 – Directional coupler length and coupling coefficient Wavelength 1.5 µm – width 1.2 µm – gap 0.6 µm
Comment results (distance needed for a complete energy transfer between waveguides, distance needed for splitting power in half.. )
deep waveguide
Paste L/Lpi vs K plot here

## Slide 6: Learning outcome #3 – 2x2 Directional Coupler Width 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
Comment results (Coupling relationship, Lpi, losses, … )
deep waveguide
Paste propagation plots and output text here

## Slide 7: Learning outcome #4 – Parallel uncoupled waveguides Wavelength 1.55 µm, width 1.0 µm, gap to be found for uncoupled wvgs
Hints:
All waveguides running in parallel are coupled somehow. Controlling the degree of coupling is key for those waveguides you don’t want coupling over certain level (i.e. uncoupled waveguides). Uncoupled waveguide definition, we will use K<0.01. Parallel waveguide length = 10 mm (typical length of a chip). Find minimum gap shallow / deep w=1.0µm wvl 1.55 µm.
deep waveguide
Paste vs gap for 10 mm wvgs to be uncoupled
shallow waveguide
Paste vs gap for 10 mm wvgs to be uncoupled

## Slide 8
Multimode Interferometer (MMI) Coupler

## Slide 9: Learning outcome #5 – Multimode Interference (MMI) Coupler cross-section
INSTRUCTOR:
Present Python and GDSFactory implementation of DC cross-section
Describe how to obtain the beating length
Describe the outputs.
ALL EXAMPLE #2: waveguide width 12 µm, gap between waveguides 0.6 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 10: Learning outcome #6 – 6.1 2x2 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results (Coupling relationship, Lpi, losses, comparison with Directional Coupler… )
deep waveguide
Paste propagation plots and console results

## Slide 11: Learning outcome #6.2 – 2x2 Multimode Interference Coupler - Optimization Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results
deep waveguide
Paste propagation plot and console results
Target: make equal ratio over outputs (even if not 0.5) and minimize excess loss (even if not 0.0 dB)
With same settings of previous LO, now adjust try to manually optimize the MMI by changing iteratively:
- Change dL_MMI
- Change I/O waveguide position +/- dy
Hints: observe the 2D EME propagation results to guide you to the best settings of a) and b).

## Slide 12: Learning outcome #6.3 – 2x2 Multimode Interference Coupler – Optimization (II) Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results
deep waveguide
Paste propagation plot and console results
Target: make ratio over outputs 0.5 + excess loss < 0.1 dB
With same settings of previous LO, now modify the notebook so I/O waveguides have a different width.
- The nominal I/O waveguide width you have been using is 1.0 µm, increase it.
(Warning! Every time you change the I/O waveguide width you have to re-run modes calculation)
Hints: observe the 2D EME propagation results to guide you to the best settings of a) and b).

## Slide 13: Learning outcome #7 – 1x4 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = ? µm
Repeat all the design process for a 1x4 MMI Coupler.
deep waveguide
Paste propagation plots and console results

## Slide 14: Extra #1 – Directional wavelength dependence Wavelengths from 1.5 to 1.7 µm, gap = 0.6 µm, width 1.0 µm
Comment results
slab = 150nm
deep waveguide
Paste vs wvl for TE and TM plot here
shallow waveguide
Paste vs wvl for TE and TM plot here

## Slide 15: Extra #2 – Directional coupler gap dependence Wavelength 1.55 µm, width 1.0 µm, gap 0.2-2.4 µm (step 0.2 µm)
Make conclusions and observations from your results
slab = 150nm
deep waveguide
Paste vs gap for TE and TM plot here
shallow waveguide
Paste vs gap for TE and TM plot here

## Slide 16: Extra #3 – MMI coupler wavelength dependence Wavelengths from 1.5 to 1.7 µm, wMMI = 6.6 µm
Comment results (Important. Compare with Directional Coupler)
slab = 150nm
deep waveguide
Paste vs wvl for TE and TM plot here
shallow waveguide
Paste vs wvl for TE and TM plot here

## Slide 17: Extra #4 – MMI coupler body width dependence Wavelength 1.55 µm, wMMI = 5-10 µm (steps 0.5 µm)
Polarization independent coupler: is there any point for which the MMI coupler can work identically for TE and TM? Answer yes / no and explain why?
slab = 150nm
deep waveguide
Paste vs width for TE and TM plot here
shallow waveguide
Paste vs width for TE and TM plot here

## Slide 18: Thank you